## Slide 1
Baby Camera
Palm Tracking Algorithm
ROS2 + MediaPipe + ONVIF PTZ camera control
Input
RTSP camera stream
Perception
Open palm detection
Control
Pan / tilt command
Output
ONVIF camera motion

## Slide 2
System Architecture
Three ROS2 nodes form a closed-loop camera controller.
Tapo Camera
RTSP stream
ONVIF PTZ target
rtsp_image_publisher
Publishes camera frames
/baby_cam/image_raw
palm_tracker
Detects open palm
Publishes Twist command
ptz_controller
Converts Twist to ONVIF
ContinuousMove / Stop
RTSP
Image
Twist
ONVIF feedback loop
Debug Output
/baby_cam/tracking_image
Annotated palm overlay

## Slide 3
Palm Detection Pipeline
The tracker only follows a stable open palm; every other state stops the camera.
Receive Image
/baby_cam/image_raw
Process Frame
frame skip
FPS gate
Convert
ROS Image to BGR
Preprocess
resize
BGR to RGB
MediaPipe Hands
21 landmarks
Hand Found
landmarks
Yes
Stop Camera
publish zero Twist
No
Continue
palm validation
Yes

## Slide 4
Palm Validation Decisions
The camera moves only when all palm checks pass.
Confident Hand
landmarks inside frame
minimum hand size
Open Palm
extended fingers >= 4
Stable Palm
stable_palm_frames
default: 2
Track Palm
compute center error
Yes
Yes
Yes
Stop Camera
reset tracking state
publish zero Twist
No
No
No

## Slide 5
PTZ Command Generation
The palm center is converted into smooth pan/tilt velocity commands.
Palm Center
average of landmarks
Center Error
palm center - image center
Filtering
error smoothing
derivative clamp
Velocity Limits
max speed
acceleration limit
Publish Twist
/baby_cam/ptz_cmd
Control equations
Error
error_x = palm_x - image_width / 2
error_y = palm_y - image_height / 2
Command
pan = error_x * pan_gain
tilt = -error_y * tilt_gain

## Slide 6
Key Runtime Parameters
These values tune responsiveness, stability, and safety.
Detection: min_detection_confidence, min_tracking_confidence
Palm quality: min_hand_size_px, min_landmark_visibility_ratio, stable_palm_frames
Responsiveness: pan_gain, tilt_gain, command_smoothing_alpha
Safety limits: max_pan_speed, max_tilt_speed, max_pan_accel, max_tilt_accel
Noise handling: center_tolerance_px, movement_start_tolerance_px, min_command_speed
Default behavior
Open palm: follow toward image center
No palm or invalid palm: stop immediately

## Slide 7
Launch and Topics
Single launch file starts the complete palm tracking camera controller.
Launch
ros2 launch baby_camera_control tapo_camera.launch.py
Input Topic
/baby_cam/image_raw
sensor_msgs/Image
Command Topic
/baby_cam/ptz_cmd
geometry_msgs/Twist
Debug Topic
/baby_cam/tracking_image
sensor_msgs/Image
Security note: keep RTSP and ONVIF on the local network and do not commit real camera credentials.